## Slide 1
Creating Standalone ROS Nodes from Simulink
ARM Lab

## Slide 2
MATLAB & Simulink
MATLAB Coder
Simulink Coder
ROS Toolbox (Simulink)
Python 2.7
Setting the Python
version in MATLAB
ARM Lab
Requirements:
Pipeline:
Creating the Simulink model
Building the model as a CPP code
Manually transferring the files to a Linux system (.sh & .tgz)
Creating a catkin_ws
Creating the package in the catkin_ws
Running the node
Setting the model parameters/hardware board settings
rosinit
Setting the active writable directory

## Slide 3
ARM Lab
Obstacle Avoidance Model from scratch (Simulink Model):
Input
Should be specified as a bus-bar. Signal size lengths can be changed via the bus-editor present on Modeling > Design tab

## Slide 4
ARM Lab
Obstacle Avoidance Model from scratch (Simulink Model):
Lateral Error
linear.x controller
angular.z controller
Lateral Error
linear.x controller
angular.z controller

## Slide 5
ARM Lab
Obstacle Avoidance Model from scratch (Simulink Model):
Publisher
Should be specified as a bus-bar. Signal size lengths can be changed via the bus-editor present on Modeling > Design tab
Max velocities on the hardware side
Change the datatype because the type upstream is ‘single’, and the publisher values are ‘double’

## Slide 6
ARM Lab
Model Parameters:
1
2
3
4

## Slide 7
ARM Lab
Building the model as a CPP code:
Set the current path where the generated code files will be stored
Transfer to a Linux system with ROS

## Slide 8
ARM Lab
Building catkin package:
With the catkin workspace already created – run the following commands
  Copy the .tgz file and the shell command file in the home directory
  Make the shell command file an executable (chmod +x <file_name>)
  Run the following commands to run the package
    cd ~
    ./build_ros_model.sh obstacleAvoidance.tgz <path to catkin_ws>
Running the node:
Start the ROS master node
Launch the turtlebot3 world in which the node will be run
Source the setup file
Run the following command (while in the workspace) to run the node
  rosrun <package_name> <node_name>
To identify the name of the node list down the files in the following directory
  /catkin_ws/devel/lib/obstacleavoidance